## Slide 1
GRIDMESH / TEAM BP
01
CHALLENGE 03 / GRID RELIABILITY
GridMesh
Solar forecasts that become feasible reserve decisions
Federated learning protects site data.
A constrained scheduler protects reliability.
Team BP · Round 1 proposal
Notes: Round-one idea proposal backed by an implemented simulation. GridMesh is the project name used by the repository; MicroWatt-FL remains the core federated forecasting concept. The neighbourhood artwork is a generated concept illustration, not a field deployment. Team and mentor names were supplied by the user and professor email.

## Slide 2
The purpose: dependable solar for neighbourhoods
GRIDMESH / TEAM BP
02
When clouds arrive, the operator faces two bad choices
Under-schedule backup
Unserved demand and fragile trust in solar
Over-schedule backup
Higher operating cost and avoidable resource use
GridMesh turns site forecasts into one auditable decision
Who benefits
Households and local businesses
Who operates it
Community operator with DISCOM oversight
What changes
Backup follows measured risk
Notes: Challenge 03 asks for affordable, neighbourhood-scale flexibility that bridges renewable intermittency and helps the DISCOM. The operating example is illustrative. The repository evaluates daytime renewable-intermittency intervals; it does not claim full feeder resource adequacy. Sources: supplied challenge statement and organizer email.

## Slide 3
A simple operator journey
GRIDMESH / TEAM BP
03
1 Solar site
Forecast locally from site history and weather
2 Coordinator
Weight updates by data volume, quality and trust
3 Node advisor
Combine demand, forecast uncertainty and asset limits
4 Operator
Approve backup schedule or flag a capacity gap
›
›
›
Raw time series stay at each site
Model updates cross the network
Dispatch remains human-approved
Layperson view
“Cloud risk increased. Schedule 8.4 MW. Asset limits leave a 0.7 MW warning.”
Notes: Proposed user journey. Each site retains raw histories and trains locally. The coordinator receives model updates and reliability metadata, then returns a shared model. Aggregate forecasts, demand and asset limits feed the scheduler. The operator receives a recommendation and capacity warning, not an automatic control command. Secure aggregation and production authentication remain roadmap items.

## Slide 4
100 local learners, one constrained decision
GRIDMESH / TEAM BP
04
FEDERATED FORECASTING / 75%
Solar sites
Past PV + weather
Local MLP / GRU / LSTM
Reliability-aware FL
FedAvg × data quality × trust
Event-aware participation
Shared forecast model
30-minute horizon
No pooled raw histories
›
›
RESERVE SCHEDULING / 25%
Node inputs
Aggregate forecast
Demand + asset limits
Causal margin
Gaussian n-sigma
or empirical tail
Daily linear program
Grid import + backup
Capacity warning
›
›
Notes: Architecture follows the professor’s suggested 75% federated-learning and 25% reserve-scheduling split. The current repository simulates 4 sites for repeated experiments and includes a 100-site scale test. Real weather and irradiance seed modelled PV power. Demand, site capacities, faults, limits and costs are simulated assumptions.

## Slide 5
Federated accuracy survives bad site data
GRIDMESH / TEAM BP
05
Chart: 
| Smart persistence | Local only | Pooled | GridMesh
Test RMSE | 0.0735 | 0.0666 | 0.0643 | 0.0641
Stale sensors at 2 of 4 sites
+8.9%
FedAvg damage to healthy sites
+0.4%
GridMesh damage to healthy sites
Five-seed headline. MLP selected over implemented GRU/LSTM in a separate 3-round screen.
Notes: Five-seed values from outputs/RESULTS.md. Normal-condition test RMSE: smart persistence 0.0735, local-only 0.0666, centralized pooled 0.0643 and reliability-aware FedAvg 0.0641 p.u. In the two-site stale-sensor scenario, healthy-site RMSE damage is +8.9% under FedAvg and +0.4% under GridMesh. These faults are simulated. The result demonstrates robustness in the simulation, not field reliability. A separate one-seed, three-round screening implemented all three architectures: MLP RMSE 0.0655, GRU 0.0693 and LSTM 0.0690. The compact MLP remains the default based on that screening.

## Slide 6
Scaling cuts traffic before it cuts accuracy
GRIDMESH / TEAM BP
06
Communication reduction
Chart: Communication (MB)
| 4 sites 20 rounds | 100 sites per round
FedAvg | 5.08 | 6.35
Event-aware | 2.55 | 3.77
100-site scale test
−41%
traffic per round
0.0649 RMSE
with event-aware participation
Stable sites skip some rounds. Drifting sites always participate.
Notes: Five-seed 4-site communication values and one-seed 100-site scale simulation from outputs/RESULTS.md. Event-aware participation sends a 16-byte heartbeat from stable clients and trains drifting clients. At 4 sites, total communication over 20 rounds falls from 5.08 to 2.55 MB. At 100 sites, per-round traffic falls from 6.35 to 3.77 MB while test RMSE remains 0.0650 vs 0.0649 p.u. This is a simulator, not a distributed network benchmark.

## Slide 7
The paper supplies the margin, not the full schedule
GRIDMESH / TEAM BP
07
Forecast error
eₜ = actualₜ − forecastₜ
Causal Gaussian margin
mₜ = max{ Φ⁻¹(1−δ) σₜ − μₜ , 0 }
Non-Gaussian check
mₜ = max{ Q₁₋δ(forecast − actual), 0 }
A 95% margin target does not override backup power or energy limits.
Notes: Research basis: Khaing, Kannan & Rao, “Accurate energy predictions for optimal power flow problems,” Clean Energy (2026), Theorem 4.3. https://doi.org/10.1093/ce/zkag018. Error convention e=actual minus forecast. The Gaussian uncertainty margin is m=max(Phi inverse of 1-delta times sigma minus mu, zero). The implementation shifts residuals by the forecast horizon so future observations cannot affect today’s margin. An empirical rolling upper quantile of forecast minus actual is the non-Gaussian benchmark. Both are margins; the scheduler separately adds the expected demand gap.

## Slide 8
A small linear program makes asset limits explicit
GRIDMESH / TEAM BP
08
1 Expected gap
gₜ = max(Dₜ − Gₜ − R̂ₜ, 0)
2 Requirement
bₜ = gₜ + mₜ
3 Daily decision
min Σ Δt(cqₜ + cₜuₜ)
Subject to
qₜ + uₜ ≥ bₜ
0 ≤ qₜ ≤ Pmax
Σ qₜ Δt ≤ Emax
uₜ ≥ 0
Operator output
Grid import + scheduled backup
+ visible capacity warning
Implemented with SciPy HiGHS. Limits and costs are configurable assumptions.
Notes: Implemented formulation in src/reserve/simulator.py. Grid import equals the smaller of its limit and the positive demand-minus-forecast gap. Expected gap is positive demand minus grid import minus forecast. Required backup adds the causal margin. For each day, the LP minimizes scheduled backup cost plus priority-weighted planned-gap cost. Constraints enforce requirement coverage, backup power and daily energy. A planned-gap variable exposes infeasibility. During real-time evaluation, scheduled backup meets realized net deficit and the remainder becomes energy not served. Daytime intermittency only; night adequacy is outside scope.

## Slide 9
Constrained scheduling improves both cost and reliability
GRIDMESH / TEAM BP
09
Five-seed means / simulation
Chart: 
| Scheduled backup (MWh) | Unserved energy (MWh) | Assumed cost (cost units)
Fixed 20% | 2420.64 | 310.01 | 8620.82
n-sigma 5% | 1575.52 | 278.1 | 7137.49
−34.9%
scheduled backup
−10.3%
unserved energy
−17.2%
assumed total cost
Nominal margin coverage and feeder availability are reported separately.
Notes: Five-seed simulation from outputs/tables/reserve_benchmark_5seed.csv. Fixed baseline uses a 20% of demand uncertainty margin. At delta 0.05, n-sigma mean scheduled backup is 1575.52 MWh versus 2420.64 MWh, unserved energy 278.10 versus 310.01 MWh, and assumed total cost 7137.49 versus 8620.82. Relative changes: minus 34.9%, minus 10.3%, minus 17.2%. Demand, PV capacities, grid limit, backup limits and costs are simulated assumptions. Weather and irradiance are real; PV output is modelled. Asset constraints still leave a planned capacity gap, which the dashboard exposes.

## Slide 10
Purpose translated into measurable value
GRIDMESH / TEAM BP
10
Judge lens | What GridMesh shows | Metric or gate
Efficiency | Less network traffic and less scheduled backup | −41% traffic at 100 sites; −34.9% backup
Sustainability | More dependable solar integration | Pilot: avoided fossil backup / curtailment
Accessibility | Local data and plain operator warnings | ₹46.50/month software hypothesis at 100 homes
Scalability | Repeatable node with sampled clients | 4-site evidence; 100-site scale simulation
Ownership
Community operator or ESCO runs the service; DISCOM receives aggregate risk and capacity alerts.
Notes: Alignment to the organizer’s efficiency, sustainability, accessibility and scalability themes. Sustainability effects are intended outcomes and require field validation. Affordability budget is an illustrative software-service boundary carried forward from the prior proposal: INR 4,650 monthly shared across 100 households equals INR 46.50 per household per month. It excludes hardware, backup energy, installation, grid bills, tax and finance. No willingness-to-pay evidence or Schneider price comparison is claimed.

## Slide 11
A focused module beside Schneider’s platforms
GRIDMESH / TEAM BP
11
Established Schneider scope | GridMesh proposal focus
DERMS coordinates distributed assets | Cross-owner federated forecast training
Microgrid Advisor forecasts and optimizes DER | Trust-weighted updates from imperfect sites
Microgrid Operation supports operational control | Human-approved reserve advice with visible gaps
Production platforms cover lifecycle and integration | Lightweight research module for small portfolios
Positioning
Complement, validate, then integrate. No replacement claim and no unsupported feature-exclusivity claim.
Notes: Public Schneider pages describe EcoStruxure DERMS, Microgrid Advisor and Microgrid Operation as broad platforms for DER coordination, forecasting, optimization and control. GridMesh does not claim Schneider lacks equivalent internal methods. The distinction is the proposal’s narrow research focus: privacy-preserving cross-owner learning, update reliability scoring and transparent feeder reserve advice for smaller portfolios. A mature module would integrate through approved interfaces after security review. Sources: https://www.se.com/ww/en/work/solutions/electric-utilities/ ; https://www.se.com/us/en/work/products/explore/ecostruxure-microgrid-advisor/ ; https://www.se.com/us/en/product-range/89571422-ecostruxure-derms/ ; https://www.se.com/us/en/product-range/65897-ecostruxure-microgrid-operation/ .

## Slide 12
Round-one ask and path to a pilot
GRIDMESH / TEAM BP
12
NOW
Audited simulator
Dashboard
Reproducible evidence
NEXT
Measured feeder data
Security + privacy review
Shadow-mode pilot
ASK
Advance GridMesh
to prototype round
Team BP
Bhavesh M · Ajay Javali · Pragun Kirani · Varshith M Gowda
Mentors
Prof. Shrisha Rao · Prof. Aswin Kannan
Notes: Current state: implemented simulation and dashboard, three model families, five-seed forecast and reserve evidence, 24 audit checks, and a 100-site scale test. Next steps are validation on measured multi-site PV and demand, secure aggregation, feeder constraints and a shadow-mode pilot. Team names supplied by the user. Mentors from the professor email and user confirmation: Prof. Shrisha Rao and Prof. Aswin Kannan.